## Slide 1: Smart Devices and Electric Vehicle Chargers for Grid Demand Response Team HAM: Ming Wang, Anthony Vu, Hongnian Yu, Arunav Singh
Advisors: Professor G.P. Li and Dr. Michael Klopfer Department of Electrical Engineering and Computer Science

## Slide 2: Introduction to Problem
California Energy Crisis
  Aging power plants
  Need clean air -> shift toward EVs
Why California?
  Leading by example, shown trend across nation
Net Load Curve

## Slide 3: What needs to be done?
Conservation & Zero Net Energy
Demand response
  Energy produced in response to demand at any given time
Reduce and add efficiency standards
  Not very significant
EVs can require more power than rest of household
  Major contributor to load issue

## Slide 4: Our Focus
Downside of increasing popularity of EVs
  Exaggeration of Net Load Curve  Demand Response
Variance of availability of energy
  Solar plentiful during day, zero during night
  Wind availability across seasons, generally more at night time
Our solution
  Schedule EV charging around time and energy availability
  Based on individual situations across seasons and variable weather patterns

## Slide 5: Vehicle Charging System
Goals
  Make sure vehicles plugged in, charged by morning
  Max resource efficiency
Two Parts
  Proof of concept of scheduling controls engine
    Bluetooth enabled OpenEVSE
  IoT enabled charger

## Slide 6: Charge Scheduling Algorithm
Simulate scheduling using prior data
  4 different months -> 4 seasons
    Solar and Wind patterns at each time of day
Effect of variable weather patterns
    Changes in wind speeds -> Affect available energy
      Demand Response
Chart: July (Summer) Power Availability
Wind | 4800000 | 4260000 | 3900000 | 3450000 | 3120000 | 2850000 | 2400000 | 1800000 | 1320000 | 1200000 | 1110000 | 1170000 | 1260000 | 1320000 | 1560000 | 2100000 | 2940000 | 3960000 | 4740000 | 5100000 | 5160000 | 5130000 | 5100000 | 5040000
Solar Thermal | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 299000 | 702000 | 897000 | 1053000 | 1072500 | 1075750 | 1079000 | 1075750 | 1072500 | 1053000 | 897000 | 702000 | 299000 | 0 | 0 | 0 | 0
Solar PV | 0 | 0 | 0 | 0 | 0 | 0 | 261000 | 1566000 | 3262500 | 4524000 | 5785500 | 6438000 | 6655500 | 6438000 | 5785500 | 4524000 | 3262500 | 1566000 | 261000 | 0 | 0 | 0 | 0 | 0
Chart: Power Generated from 1 MW turbine
| 4.1 | 4.15 | 4.2 | 4.3 | 4.6 | 5 | 5.2 | 5.4 | 5.4 | 5.4 | 5.5 | 5.5 | 5.6 | 5.7 | 5.9 | 6 | 6.1 | 6.3 | 6.4 | 6.4 | 6.45 | 6.5 | 7 | 6.6.
 | 77.5 | 80 | 80 | 85 | 100 | 100 | 120 | 150 | 140 | 140 | 145 | 150 | 160 | 175 | 195 | 200 | 210 | 235 | 250 | 260 | 265 | 280 | 295 | 285

## Slide 7: Charge Scheduling Algorithm

## Slide 11: Scheduling Controls Engine
Simulation set up
  5PM-8AM
  Real Node/Virtual Node

## Slide 12: Scheduling Controls Engine
Features
  Add EV
  Change wind speed
  Check EV status

## Slide 13: Simulation Result

## Slide 14: IoT Enabled OpenEVSE
Wifi-Enabled NodeMCU ESP8266
MQ Telemetry Transport
Reliable and stable control across network

## Slide 16: Further Development and Impact
In future, scheduling controls GUI will be have full control over IoT enabled devices
  Merge both sides of our project
Covered by California Public Utilties commission as rebate program
  Cost of unit and use

## Slide 17: Competition & Alternative Solutions
AeroVironment TurboCord
  No charge scheduling
  No smart capability
What makes our system unique?

## Slide 18: Summary
Energy climate is rapidly changing
  Inherent variance in renewable energy availability
  Demand response must be controlled
    Energy must ALWAYS be available
  EVs have great impact but…
Our System
  Utilities have window into residences
    True IoT system and MQTT framework
    Reliable interaction

## Slide 19: Acknowledgements
A big thanks to our mentors:
Professor G.P. Li and Dr. Michael Klopfer
Calit2/Calplug and Microsemi in collaboration with Smartenit LLC
for guidence and direction in our project.
Thank you to our contributors: